PARAMETERS ESTIMATION OF THE AIRCRAFT’s LONGITUDINAL and LATERAL MOVE

Mihai LUNGU,  Ph.D. student

Avionics Division, Faculty of Electrical Engineering, University of CRAIOVA, ROMANIA, E-mail: Lma1312@yahoo.com

Abstract – This paper deals with an analysis regarding identification and control of stability processes of an aircraft’s longitudinal and lateral move. The estimation of the transfer function for a stabile flight of an aircraft (longitudinal move) isn’t made using the most important estimation method (the least square method). Other three methods (origin pole compensation method, instrumental variables method and prediction error method – with the two variants) are used here to estimate all the coefficients of the transfer function of the longitudinal move of an aircraft. All these methods estimates the transfer function by the continue minimization of the error function. The lateral move model’s parameters are estimated using the least square method. Thus, a simulation program for discrete transfer function determination of the lateral move, for stabilization analyses and for time characteristics plotting of the leading system and estimated system output in random perturbation conditions is made; estimation errors are being calculated.

Keywords: estimation, residues, longitudinal, lateral, transfer function

1. INTRODUCTION

We consider the longitudinal move of an aircraft. One presents in the following pages some methods used for aircraft’s longitudinal and lateral moves identification. These methods calculate the coefficients of the transfer function in closed loop. It doesn’t matter if the system is stable or not. The most important thing is superpose of the estimated system’s response and the leading system’s response.

2. THE ORIGIN POLE   COMPENSATION (CMMPM)

A state estimator must assure the controllability of the system whose parameters are estimated, indifferent to adaptive structure. The least square method doesn’t always give models characterized by controllability. That’s why in some cases it must be modified.

The system, whose parameters must be determined, is described by the equation

(1)

where  is the delay operator and the polynomials  and  are

(2)

The estimated model  of the leading system (aircraft), obtained by an parametric identification method, may be described by equation

(3)

where  is the noise applied to  the model and the polynomials  and  have expressions

(4)

CMMP algorithm (least square algorithm) modification is based upon the discrete transfer function modification through origin pole  compensation. The modified CMMP algorithm (CMMPM) builds a convergent vector  and with it the vector of the estimated parameters [1]

(5)

Thus, the coefficient  is almost non-null.

The control law may be chosen of general form

(6)

with the polynomials

(7)

The closed loop system is described by equation [1]

(8)

where

(9)

and

(10)

is white noise.

3. INSTRUMENTAL VARIABLES METHOD (MVI)

This method is a generalization of CMMP. It gives the estimated parameters only for the determinist part of the model  and not for the parameters of the polynomial  associated to the random perturbation. The leading system model  is described by the equation (1) and the one of the estimated model  by equation (3); in this equation one considers  The equation equivalent to equation (3) is

(11)

By multiplication of this equation with  instrumental variable vector (whose elements haven’t physic significations, they are only necessary “instruments” for the  estimation), one obtains the equation of estimator.

(12)

or

(13)

where  is the measurements number; the vector  may be chosen different ways. Let vector  be [2]

(14)

where ; if  and are the  and  polynomials estimations, one chooses

(14)

Let the transfer function associated to the longitudinal move of an aircraft be

(15)      (15)

The calculus program is presented in Appendix 1. The input  and perturbation  of the leading system are random type. For the parameters estimation of the vector  one uses, in Matlab medium, the operator iv4. Using the instruction resid the residues associated to this method are calculated and plotted (figure 1). In figure 2 frequency characteristics (amplitude-frequency and phase-frequency) for the leading system and for the estimated system (using CMMP and MVI methods) are plotted.

Figure 1: Residues of CMMPM method

Figure 2: Frequency characteristics for CMMP and MVI methods

The discrete transfer function is

(16)

4. THE PREDICTION ERROR METHOD (MEP)

This method is more complicated than the others, but it is more precisely. MEP calculates the coefficients of the polynomials  and the coefficients of the polynomials that “modify” perturbation which affects the leading system. Starting from an initial estimation, one calculates the parameter of the system through successive iterations till the convergence criteria is reached. The initial estimations used by MEP may be obtained using one of the previous methods [2].

The prediction error is the perturbation

(17)

The leading system is described by equation

(18)

Thus, the residue is

(19)

The estimated parameters (the vector) are determined through the sum’s minimization of the square prediction errors

(20)

where  is the available data number. An estimation algorithm is the following one [2]:

1) one makes an initial estimation of the coefficients of  using a CMMP type method, and thus it results

2) using the previous estimation  one calculates filtering signals

(21)

one determines the estimations  and  of

the polynomials  and ;

(22)

4)   hereby a new estimation  is calculated [3]

(23)

where  is expressed function of assessments   and  from previous step;

(24)

The calculus formula for  is

(25)

4.1. Parameters estimation of the output error model

Calculus program is presented in Appendix 2.

Instead of ARX, or iv4, one uses the instruction oe with a similar syntax.

Estimated transfer function is

(26)

The curves  and  are plotted in figure 3.

Figure 3: The outputs  and

4.2. Parameters estimation of the ARMAX model

Calculus program is presented in Appendix 3. Instead of instruction oe one uses instruction ARMAX.

The estimate transfer function is

(27)

The curves  and  are plotted in figure 4. The frequency characteristics [4,5] (amplitude - frequency and phase-frequency) are plotted in figure 5 (1 – CMMP, 2 – MVI, 3 – ARMAX, 4 – frequency characteristics of the leading system).

Figure 4: The outputs  and

Figure 5

Figure 5: Comparative frequency characteristics

5. LATERAL MOVE ANALYSIS

Lateral move aircraft dynamics may be described by the matriceal equations with non-dimensional variables [6]

(28)

in which

(29)

is the side-slip angle,  and  are respectively the yaw and roll angular velocities, - the roll angle, - the rudder deflection, - the aileron deflection ( and  are expressed in degrees).

For the following coefficients of an heavy aircraft [6], which flies at , with ,  using a Matlab program, one obtains matrices  and  of the linear system (28) while the vectors  and  are chosen from the second equation (28).

is the state vector,  - elevator deflection. Choosing as output variable  - the pitch angle, it results

With these values, using a Matlab program, is obtained matrix  and the vectors;

(30)

The program also calculates the transfer functions

(31)

(32)

(33)

(34)

The calculated eigenvalues are:

In fig.6 Dirac impulse’s responses  are represented (all the amplitudes are expressed in radians).

Figure 6: Dirac impulse’s responses

The program also calculates the matrices associated to the discrete mode

(35)

Figure 7: Step responses of the discrete mode

In fig.7 step responses of the discrete mode (with the amplitudes  and) are represented. The discrete transfer functions are

(36)

(37)

(38)

(39)

while the discrete eigenvalues are

So, the discrete model of the aircraft’s lateral move may be described by the following metriceal equation

(40)

6. PARAMETRIC IDENTIFICATION ALGORITM

Calculus algorithm for a parametric estimator is based on the least square method [7].The estimated parameters of the  model are permanently modified with an adaptation mechanism, based on the continue measure and the minimization of the error function.

One makes the vector

the  matrix and the vectors

(41)

The estimated parameters vector  may be obtained through minimisation of the square indicator

(42)

From minimum of  condition [7], that means  one results

(43)

One makes the notations

(44)

where  and , and  is the sample period and

(45)

The recurrence relation between ( the covariance matrix) and  is [2, 3]

(46)

where  represents the forget factor, and the recurrence relation between  and

(47)

The discrete transfer functions of   are (31)(34), while the discrete transfer functions of   may be obtained using a Matlab program

(48)

(49)

(50)

(24)

Figure 8: Parametric identification scheme

In this program, first matrices  and  are formed (they contain the coefficients of the four transfer functions). The input  and perturbation  of the leaded system are chosen as random type. For the  parameters of model  estimation one uses ARX operator from Matlab, which has the following syntax th=ARX(z,nn), where  - output data matrix  and the input ; nn-defines the denominator order (), numerator order () and the model’s delay (); th returns the estimated parameters in theta format (the elements of the vector ) using the least square method. The program plots the characteristics  and, presented in fig. 9;  is the output of the leaded system  and  - the output of the estimated model (). In fig. 9 one also presents the perturbation [7].

In fig.9 the following characteristics families are presented:  as responses to random input signal  and random perturbation fig.9.a;  as responses to random input signal  and random perturbation fig.9.b;  as responses to random input signal  and random perturbation fig.9.c;  as responses to random input signal  and random perturbation fig.9.d.

a.

b.

c.

d.

Figure 9: Lateral Parametric identification

The Matlab program used for least square method identification is presented in Appendix 4.

7. APPENDIX

Appendix 1

close all;clear all;

A=[1 -1.6041 0.2776 0.302 0.0352];

B=[1.2449 -1.2248 -0.0513 0.0485];

tho=poly2th(A,B); u=idinput(300,'rbs');

e=randn(300,1); y=idsim([u,e],tho);z=[y,u];

th=iv4(z,[4 4 0]);

%Calculul si reprezentarea grafica a reziduurilor

ee=resid(z,th); h=figure; plot(ee);

title('Reziduurile metodei variabilelor instrumentale'); xlabel('Timp [s]');grid;

%Compararea functiilor de transfer obtinute prin iv4,arx si metoda de analiza spectrala

[GS,NSS]=spa(z); [Ga,NSa]=trf(tho);Gi=trf(th);

h=figure;bodeplot([GS Ga Gi]);

grid; present(tho); present(th)

Appendix 2

close all;clear all;

F=[1 -1.6041 0.2776 0.302 0.0352];

B=[1.2449 -1.2248 -0.0513 0.0485];

tho=poly2th(1,B,1,1,F,1);

u=idinput(100,'rbs');e=randn(100,1);

y=idsim([u,e],tho);z=[y,u]; th=oe(z,[4 4 0]);

present(tho); present(th);

%Reprezentarea grafica a raspunsurilor sistemului condus si modelului

y1=idsim([u e],th); plot(y);

title('Semnalele de iesire ale sistemului condus si modelului'); xlabel('Timp [s]');

hold on;plot(y1,'r');grid;

Appendix 3

close all;clear all;

A=[1 -1.6041 0.2776 0.302 0.0352];

B=[1.2449 -1.2248 -0.0513 0.0485];

tho=poly2th(A,B);u=idinput(300,'rbs'); e=randn(300,1);y=idsim([u,e],tho); z=[y,u];

th=armax(z,[4 4 0 0]); i=iv4(z,[4 4 1]);

res=resid(z,th); [GS,NSS]=spa(z);

[Ga,NSa]=trf(tho); Gi=trf(i);Ge=trf(th)

bodeplot([GS Ga Ge Gi]); grid;

present(tho); present(th);

y1=idsim([u,e],th);h=figure;plot(y);

grid;hold;plot(y1,'r'); xlabel('Timp [s]');

Appendix 4

close all;clear all;

%Intrarea 1, iesirea 1

A=[1 -3.0442 3.5019 -1.7912 0.3403];

B=[-1.58 4.2814 -3.9394 1.2182];

tho=poly2th(A,B);

u11=idinput(300,'rbs');e11=randn(300,1);

y11=idsim([u11,e11],tho);

z=[y11,u11];th11=arx(z,[4 4 0]);

yc11=idsim([u11,e11],th11);

subplot(211);plot(y11); grid; hold; plot(yc11,'r');

title('Variatia in timp a iesirilor modelului si sistemului condus cu intrarea 1, iesirea 1');

subplot(212); plot(e11); grid; title('Perturbatia e11'); xlabel('Timp[s]');

%Intrarea 1, iesirea 2

A=[1 -3.0442 3.5019 -1.7912 0.3403];

B=[0.039 -0.4514 -0.1676 0.0732];

tho=poly2th(A,B);

u12=idinput(300,'rbs');e12=randn(300,1); y12=idsim([u12,e12],tho);

z=[y12,u12];th12=arx(z,[4 4 0]);

yc12=idsim([u12,e12],th12);

h=figure; subplot(211); plot(y12);

grid; hold; plot(yc12,'r');

subplot(212); plot(e12); grid;

title('Perturbatia e12'); xlabel('Timp[s]');

%Intrarea 2, iesirea 1

A=[1 -3.0442 3.5019 -1.7912 0.3403];

B=[0.3880 -1.0484 1.0157 -0.3406];

tho=poly2th(A,B);

u21=idinput(300,'rbs'); e21=randn(300,1);

y21=idsim([u21,e21],tho); z=[y21,u21];

th21=arx(z,[4 4 0]);yc21=idsim([u21,e21],th21);

h=figure; subplot(211); plot(y21); grid;

hold; plot(yc21,'r'); subplot(212);plot(e21); grid;

title('Perturbatia e21'); xlabel('Timp[s]');

%Intrarea 2, iesirea 2

A=[1 -3.0442 3.5019 -1.7912 0.3403];

B=[1.2585 -0.384 -0.9573 0.4866];

tho=poly2th(A,B); u22=idinput(300,'rbs');

e22=randn (300,1); y22=idsim ([u22,e22],tho);

z=[y22,u22]; th22=arx(z,[4 4 0]);

yc22=idsim([u22,e22],th22);

h=figure; subplot (211); plot(y22); grid;

hold; plot(yc22,'r');

title('Variatia in timp a iesirilor modelului si sistemului condus cu intrarea 2, iesirea 2');

subplot(212); plot(e22); grid;

title('Perturbatia e22');xlabel('Timp[s]');

8. CONCLUSIONS

The identification of the aircraft’s longitudinal move is achieved using four methods in Matlab medium. One observes that all the methods are very good and the transfer functions  and  are very near-by. Is not important if the system, describing longitudinal move of an aircraft, is stabile or not. The most important thing is that the time characteristics  and  are almost the same. That may be proved by the fact that the coefficients of the transfer function  are near-by to those of .

The identification of the aircraft’s lateral move is achieved using the method of the least square and a program in Matlab medium, which has as most representative command the command ARX. One may observe that superpose of the system’s outputs and leading system’s outputs is almost perfect.

References

[1] Teodorescu, D. Modele stohastice optimizate. Editura Academiei Române, Bucureşti, 1982.

[2] Tertişco, M., Stoica, P., Popescu, Th.  Identificarea asistată de calculator a sistemelor. Editura Tehnică, Bucureşti, 1987.

[3] S.Călin, Th.Popescu, B.Jora, V.Sima:Conducerea adaptivă şi flexibilă a proceselor industriale. Editura Tehnică, Bucureşti, 1988.

[4] I.Filip: Structuri şi algoritmi de conducere adaptivă. Editura Orizonturi universitare, Timişoara, 2002.

[5] M.Krstic, I.Kanellakopoulos, P.V. Kokotovic: Nonlinear and adaptive Control Design. John Wiley & Sons, New – York, 1995.

[6] V.A.Bodner: Teoria avtomaticeskogo upravlenia  poletom. Izd. Nauka, Moscova, 1964.

[7] M.Sharma, D.G.Ward: Flight – Path Angle Control Via Neuro–Adaptive Backstepping. Published by American Institute of Aeronautics and astronautics, 2002.