ON – LINE PARAMETRIC IDENTIFICATION AND DISCRETE OPTIMAL COMMAND OF FLYGHT OBJECTS

Romulus LUNGU, Dipl. Eng., Ph.D., Mihai LUNGU, Dipl. Eng. Ph.D. student

Avionics Division, Faculty of Electrical Engineering, University of Craiova, Romania, romulus_lungu@yahoo.com, lma1312@yahoo.com

Abstract ( This paper presents a new ON-LINE parametric identification and discrete optimal command algorithm for mono or multivariable linear systems. The method may be applied with good result to the automatic command of the flying object movement.

The simulation results obtained with this real time algorithm, with parametric identification of an air-air rocket’s movement in vertical plain regarding to target’s line are presented.

Keywords: parametric identification, algorithm, rocket

1. INTRODUCTION

Because of fast flying parameters’ modify for the modern aircraft and rockets, performing real time identification and optimal or adaptive command algorithms have to be made. The authors of this paper have made such an algorithm.

First of all, an off-line parametric identification is made, without command, for obtaining the initial values of these parameters for the on-line identification process.

Using the leading system  and model’s outputs, a discrete optimal command law is projected, using a quality quadratic criterion, which assures the convergence of the difference between leading system and model’s outputs. The model’s parameters, obtained by the ON-LINE identification, are used for he command law calculus.

For the algorithm validation one uses as example the automatic command of the ’s movement in vertical plain; time characteristics, representing evolution of state variables of  and their estimate, are plotted. These variables’ stabilization and the convergence of the errors  happen in maximum 2 seconds.

The proposed algorithm produces very good results in the case of longitudinal and lateral movement’s stabilization for transport and fights aircrafts.

2. CONTINOUS AND DISCRETE MODELS FOR

The leading system (the movement of ) may be described by the input – output equations with general

forms

(1)

(2)

where  is the state vector ,  the command vector , the system matrix , matrix , output vector , measurement system matrix  The estimated model is described by equations

(3)

(4)

where  is the state ’s estimation, - output ’s estimation,  and estimate matrices.

The discrete variants of equations systems (1), (2), and (3), (4) are, respectively

(5)

(6)

(7)

(8)

matrices  and  are discrete variants of matrices  and .

Another description form for the estimated system  ( dynamics estimation) [1] is

(9)

or

(10)

where

(11)

with

(12)

(13)

with

(14)

If , then equation (10) becomes

(15)

if , then  matrix can not be multiplied wit  vector because of their dimensions. That’s why, in equation (15) the last term is expressed for each concrete case (function of  and  values). So that, in the case presented below (rocket’s movement in vertical plain)  and equation (15) becomes

(16)

where

(17)

is a  vector,  is a  vector and

For command law  obtaining, one chooses the performance indicator

(18)

where  is the imposed output vector while and  are symmetric and positive definite matrices, nonsingular matrix;  has the form (17). The optimal command is obtained from optimum condition

(19)

for  has the expression

(20)

and  matrices may be calculated using ALGLX algorithm proposed by the authors of this paper or other algorithms [3], [4], [5].

3. ’S PARAMETERS IDENTIFICATION

First of all the off – line system ’s parameters identification is made, using, for example, the least square method (LSM), resulting the parameters vector ; in this moment the system’s command is uncoupled, therefore the system is an open loop one.  is then computed and the vectors  and are memorized. Also, the covariance matrix  is memorized at the end of identification. Then, matrices  are computed and with these state vectors  and  are computed; these vectors (at the end of identification) are memorized.

For simulation of time varying of ’s parameters, the parameters of  are modified (for example with 5%) and with the new coefficients  and  matrices are computed.

The loop is then closed (one adds  command) and  and  matrices are computed with ALGLX algorithm in rapport with  and  matrices and after that the matrix  is calculated.

matrix from (20) is obtained with  extracted from  Then command  is computed with (19).

The vectors , ,  and are calculated; vectors  and  are memorized and the error  is computed.

The actualization of covariance matrix is made with formula [1]

(21)

and, with this,

(22)

where  has the form (13).

State variables and  are plotted.

4. IDENTIFICATION AND OPTIMAL COMMAND OF THE ROCKET’S MOVEMENT

For the identification and discrete optimal command algorithm’s validation, present above, a simulation program was made in the MATLAB medium.

Considering model of ’s movement in rapport with equal signal line [6], [7], with state vector  and  are lateral deviation and lateral deviation angular velocity, respectively,  - incidence angle variation,  - pitch angular velocity .

With flying parameters’ values from [8], for the 40th second of flight, following step by step the algorithm, one obtained successively the results

and  vector of the system with optimal command

Also one obtained .

In fig.1 state variables  and are presented (with blue and  with red).

Fig.1 – Time varying of  and

5. CONCLUSIONS

The paper presents an ON – LINE parametric identification and discrete optimal command algorithm for linear systems. For validation, it is used to automatic command of a rocket’s movement in vertical plain with respect to equal signal line, which materializes target line. A simulation program based to presented algorithm was made in Matlab/Simulink. The obtained graphic plots express time evolution of the state variables  and the evolution of command.

References

[1] P. Eykhoff, Identificarea sistemelor. Editura Tehnica, Bucuresti, 1977.

[2] Mc. Donald, Automatic Flight Control Systems. New York–London–Sydney–Tokyo-Singapore, 1990.

[3] L. Ljung, J. Sjoberg, H. Hjalmarsson, Identification, Adaptation, Learning –The Science of Learning Models from Data, Edited by S. Bittoni, Springer Verloy Berlin Heideberg, 1996.

[4] J.W. Choi, A Simultaneous Assignment Methodology of Right/Left Eigenstructures. IEEE Transactions on Aerospace and Electronic Systems, 1998, pag. 625 – 634.

[5] J.W. Choi, LQR Design with Eigenstructure Assignment Capability. IEEE Transactions on Aerospace and Electronic Systems, vol. 35, Nr. 2, April, 1999, pag. 700 – 707.

[6] R. Lungu, Sisteme de dirijare aerospatiala. Editura Sitech, Craiova, 2002.

[7] M. Lungu, Calculul vitezelor de apropiere si deviatie de la linia tintei. The International Symposium on Naval and Masine Education. Vav – MAR – EDU 2001, Section Military Scienece, pag. 113-119 in Procedings, Constanta, May 24-26, 2001.

[8] I. Aron, R. Lungu, Automate de stabilizare si dirijare. Editura Militara, Bucuresti, 1991.